## Slide 1: (U) FLYTHRU Plans
Wally Westlake
Principal Mechanical Engineer

## Slide 2: (U) FLYTHRU Plans
FLYTHRU Requirements:
  What does it need to do?
Approach:
  How?
Interface:
  Database
  API Calls
Testing:
  With close agreement in the delayed source and transmission, rest of problem is geometry, answers should be very close

## Slide 3: FLYTHRU Requirements*
Prompt
  Calculate prompt environment (any available in RES)
  Calculate at follower location relative to intercept of leading RB
    Assume same trajectory with time offset, downrange offset, crossrange offset
  Calculate prompt environments as a function of leading RB altitude at intercept
    Specify minimum, maximum, and number of altitudes for calculation
Sustained (Delayed) Radiation
  Calculate integrated delayed dose (integral and dose rate) for along RB trajectory for follower weapon as it “flies through the debris cloud” (FLYTHRU)
  Environments
    Total Ionizing Dose in silicon (n, g, 2g)
    Number fluence
    Others:
      Energy Fluence
      1 MeV equivalent fluence
      Fission Heating?
* FLYTHRU System Requirements Document 8/2018

## Slide 4: Approach: Prompt
Geometry
  Calculate slant range and angle based on time offset, down/cross range offset
  Options:
    Assume velocity is constant from leading RB altitude to following RB altitude – Calculate distance up trajectory using constant velocity
    Integrate distance using velocity as function of time from intercept altitude up to time offset
Environments
  Use RES to calculate environment at point using slant range and angle
  Same calculations apply when looping over intercept altitude
Crossrange
Offset
Downrange Offset
Time
Offset
Leading RB Intercept Alt

## Slide 5: Approach: Sustained Radiation
Geometry
  Sustained radiation comes from fission debris cloud (fireball at early times)
    Expands in radius as function of time
    Rises vertically as function of time
    Spherical at early times, toroidal at late times
Integration
  Find time of closest approach
  Subdivide time from leading RB intercept to follower RB reaches desired HOB into time steps
    Makes sure time steps include time of closest approach
  Calculate dose rate at each time using:
    Debris Cloud Geometry data
    Emission rate from debris cloud
    Transport from debris cloud to target
Time of Closest Approach
Crossrange
Offset
Time
Offset
Debris Cloud rising with time
Downrange Offset

## Slide 6: Debris Cloud Geometry Data
Proposed Debris cloud geometry (modified point source with evacuated fireball)
  Spherical geometry of debris cloud from MAZe hydrocode runs
  Height and radius versus time as a function of intercept (or builder) yield and height of burst
  Interpolate size on yield, height of burst, time
  Radiation source located on sphere of debris within fireball
  Spherical evacuated fireball at lower density than ambient
  Data stored in SQL database with environments
  Yld = 0.1kT - 30 Mt, SHOB = 0-2000 ft/kT^1/3, t = 0-60 s
RhoR = RhoR in Fireball +
Ambient RhoR from surface
Slant range
Based on debris sphere
To target

## Slide 7: Delayed Neutron/Gamma Emission Rate
Emission Rate
  Fission debris emits neutrons and gammas at a time dependent rate that is proportional to the amount of fission during the detonation – This is the radiation source
  Three (or more) sources of emission rate data
    STYOUT has emission rate curve fit to experimental data
    Nuget/eNWEDS used data from running CINDER calculations
    Direct experimental data (Fisher-Engel)
  STYOUT data does not include neutrons or spectra information
  CINDER results from isotopes activated by fast neutron spectrum, ENDFbVII cross sections
Proposed
  Use CINDER data, interpolate rate vs time

## Slide 8: Delayed Source Rate – U235
Almost Exact Agreement for U235

## Slide 9: Delayed Source Rate – U238
Slightly higher for STYOUT – 15-30% higher

## Slide 10: Delayed Source Rate – U239
STYOUT predictions up to 1.7x higher at early times

## Slide 11: Experimental Data vs CINDER Data - Pu239
EDB is Fisher-Engle Data (original eNWEDS data)

## Slide 12: Experimental Data vs CINDER Data – U235
EDB is Fisher-Engle Data (original eNWEDS data)

## Slide 13: Experimental Data vs CINDER Data – U238
EDB is Fisher-Engle Data (original eNWEDS data)

## Slide 14: Radiation Transport
Predict amount of radiation reaching target given divergence and atmospheric scattering, extinction, and moderation
  STYOUT has single “build-up” factor curve as function of integral density (rhor)
    Only applies to primary gammas
    Unsure of origin
  Legacy FLYTHRU used RANC methodology, presumably fits to DO calculations
  eNWEDS uses transmission matrices calculated with MCNP/ADVANTG
    Primary/Secondary Gamma and neutrons
    Delayed source spectra folded with transmission matrices provides precalculated Dose/Fission Yield as a function of Slant range/RhoR and time after burst
      Ionizing dose in Si, Fluence, and 1-MeV fluence precalculated and already loaded in Sqlite database
      Could add other response types (fission heating) by folding with transmission matrix
  eNWEDS data can be applied to any altitude with mass-integral scaling
Propose using eNWEDS transmission data for radiation transport
  Precalculated dose/kt curves as function of time, isotope, and response function

## Slide 15: (U) Comparison of STYOUT delayed radiation with eNWEDS
Delayed Build-up Factor from STYOUT:
  Ratio of dose at source divided by 4πR2Dose as a function of density (ρR)
  eNWEDS Build-up factor is based on delayed source spectra at early time = 1.e-6
  No information about STYOUT spectrum, eNWEDS uses isotope and time-dependent spectrum
  Even with these uncertainties, agreement is very close within 300 g/cm2

## Slide 16: Compare Radiation Transport (build-up factors) for STYOUT
  Ratio of dose at source divided by 4πR2Dose as a function of density (ρR)
  No information about STYOUT spectrum, eNWEDS uses isotope and time-dependent spectrum
eNWEDS versus STYOUT build-up factors - Good agreement in main region of interest ( < 300 g/cm2) (10 kft slant range near ground)

## Slide 17: Genfit_dose.dll Interface
To do a prompt dose calculation
  constructDatabase(handle);
  openDatabase(handle, filename, fname_len );
  setDevice(handle, primDevice, primDeviceYield, secondDevice, secondDeviceYield);
  addEnvironment(handle, dosekind, kindEnv, ishld, constraintvalue, neutronflag, gammaflag, secondarygammaflag, xrayflag);
  setGeometry(handle, heightofburst, angle);
  calculateDoseToRange(handle, slantrange, dose);
To do a delayed dose calculation on a trajectory
  constructDatabase();
  openDatabase();
  setDevice();
  addEnvironment();
  setTrajectoryGeometry( handle, heightofburst, velocity, gamma, downrange, crossrange, timeoffset );
  calculateDelayedDoseTraj(handle, dose);

## Slide 18: Interface (cont)
To do a delayed dose calculation non-moving target
  constructDatabase();
  openDatabase();
  setDevice();
  addEnvironment();
  calculateDelayedDose(handle, slantrange, dose);
  Or calculateDelayedDoseX(handle, hot, xrange, dose);

## Slide 19: Status of New FLYTHRU
Data
  Debris cloud data loaded into RES database
  Transmission data loaded into RES database
Code
  Interface calls added to “Genfit_dose.dll”
  Interpolation of debris cloud geometry complete
  Dose calculation using mass integral scaling complete
  Code complete for delayed dose integration along straight line trajectory
  Code complete for delayed dose for non-moving target
Testing
  Delayed dose for non-moving target running and comparing reasonably well with eNWEDS
  Delayed dose verification with Nuget shows close agreement for similar modeling assumptions
  Delayed dose along trajectory working, preliminary verification with Nuget
    More detailed analysis needed

## Slide 20: Verification with Nuget – Non-moving Target
  20 kt builder at 4000 ft altitude
  Non-Moving target at 2000 ft altitude, Dose integrated over 0-60 seconds
  Horizontal range varied from 0 – 7200 ft
  Many delayed options in Nuget: This Nuget run used LAMB debris cloud, KSC source definition, point source geometry with normal air transport, only one other option tried
  Non-moving verification takes out complexity of fireball geometry and trajectory
  Very good agreement for source rates, and transport calculations

## Slide 21: Verification with Nuget - Trajectory
  20 kt builder at 4000 ft altitude
  Nuget unclassified trajectory with VRE = 25500, GRE = 45
  Time offset = 2 seconds, Downrange offset 500 ft, Crossrange offset = 0 ft
  FLYTHRU prototype used constant velocity averaged over time from time of leading RB intercept to follower RB reaching HOB.
    Probably need to add capability for time varying trajectory
  Nuget – Integrated dose = 8196 Rad-Si, new FLYTHRU = 9709 Rad-Si
  This was a rough first try, need to examine trajectory and debris cloud geometry in detail
Zoom in on Peak

## Slide 22: Tasks to complete FLYTHRU
Code integration
  Add trajectory inputs to RES input XML file
  Calculate geometry for FLYTHRU prompt slant range and angle
  Add FLYTHRU run mode to RES
    Add looping over leading RB intercept altitude
  Add delayed calls from RES to genfit_dose.dll
Testing
  Unit tests for all trajectory inputs
  Unit tests for delayed dose calculations
Algorithm
  Optimize time steps based on time after burst and slant range

## Slide 23: Tasks for FLYTHRU (cont)
Verification
  Detailed Comparison delayed dose results with other codes (FLYTHRU, STYOUT, Nuget, …)
Data
  Compare debris cloud geometry with thermal fireball data from eNWEDS – Thermal fireball data has more yields, heights of burst. Debris cloud size and height might not be smooth for low HOB due to dust sweep-up?
  Add Fission heating and PDOI responses to transport data?
  Port non-spherical cloud debris geometry from eNWEDS and optimize?